## Slide 1: CS 610: GPU Architectures and CUDA Programming
Swarnendu Biswas
Semester 2020-2021-I CSE, IIT Kanpur
Content influenced by many excellent references, see References slide for acknowledgements.

## Slide 2: Rise of GPU Computing
GPUs are now used in different applications
  Game effects, computational science simulations, image processing and machine learning, linear algebra
Several GPU vendors like NVIDIA, AMD, Intel, QualComm, and ARM

## Slide 3: Enter NVIDIA and CUDA
NVIDIA released GeForce 8800 GTX in 2006 with CUDA architecture
  General-purpose ALU and instruction set for general-purpose computation
  IEEE compliance for single-precision floating-point arithmetic
  Allowed arbitrary reads and writes to shared memory
Introduced CUDA C and the toolchain for ease of development with the CUDA architecture

## Slide 4: GPU Architecture

## Slide 5: Key Insights in GPU Architecture
GPUs are suited for compute-intensive data-parallel applications
  The same program is executed for each data element
  Less complex control flow
Multi-core chip
  SIMD execution within a single core (many ALUs performing the same
instruction)
  Multi-threaded execution on a single core (multiple threads executed concurrently by a core)

## Slide 6: Key Insights in GPU Architecture
Much more transistors or real-estate is devoted to computation rather than data caching and control flow

## Slide 7: Key Insights in GPU Architecture
GPUs do not reduce latency, they aim to hide latency
The focus is on overall computing throughput rather than on the speed of an individual core
  High arithmetic intensity to hide latency of memory accesses
  Large number of schedulable units

## Slide 8: Floating-Point Operations per Second for the CPU and GPU

## Slide 9: Memory Bandwidth for CPU and GPU

## Slide 10: High-end CPU-GPU Comparison
 | Xeon 8180M | Titan V
Cores | 28 | 5120 (+ 640)
Active threads | 2 per core | 32 per core
Frequency | 2.5 (3.8) GHz | 1.2 (1.45) GHz
Peak performance (SP) | 4.1 TFlop/s | 13.8 TFlop/s
Peak mem. bandwidth | 119 GB/s | 653 GB/s
Maximum power | 205 W | 250 W
Launch price | $13,000 | $3000
Release dates
Xeon: Q3’17
Titan V: Q4’17

## Slide 11: Compare GPU to CPU Architecture
Aims to reduce memory latency with increasingly large and complex memory hierarchy
Disadvantages
  The Intel I7-920 processor has some 8 MB of internal L3 cache, almost 30% of the size of the chip
  Larger cache structures increases the physical size of the processor
  Implies more expensive manufacturing costs and increases likelihood of manufacturing defects
Effect of larger, progressively more inefficient caches ultimately results in higher costs to the end user

## Slide 12: CPUs vs GPUs
CPUs
Designed for running a small number of potentially complex tasks
  Tasks may be unconnected
  Suitable to run system software like the OS and applications
Small number of registers per core private to a task
  Context switch between tasks is
expensive in terms of time
  Register set must be saved to memory and the next one restored from memory
GPUs
Designed for running large number of simple tasks
  Suitable for data-parallelism

## Slide 13: CPUs vs GPUs
CPUs
Small number of registers per core private to a task
  Context switch between tasks is
expensive in terms of time
  Register set must be saved to RAM and the next one restored from RAM
GPUs
Have a single set of registers but with multiple banks
  A context switch involves setting a bank selector to switch in and out the current set of registers
  Orders of magnitude faster than
having to save to RAM

## Slide 14: Advantages of a GPU
Performance of Xeon 8180M and Titan V (based on peak values)
  3.4x as many operations executed per second
Main memory bandwidth
  5.5x as many bytes transferred per second
Cost- and energy-efficiency
  15x as much performance per dollar
  2.8x as much performance per watt
GPU’s higher performance and energy efficiency are due to different allocation of chip area
  High degree of SIMD parallelism, simple in-order cores, less control/sync. logic, less cache/scratchpad capacity

## Slide 15: GPU Disadvantages
Clearly, we should be using GPUs all the time
GPUs can only execute some types of code fast
  SIMD parallelism is not well suited for all algorithms
  Need lots of data parallelism, data reuse, & regularity
GPUs are harder to program and tune than CPUs
  Mostly because of their architecture
  Fewer tools and libraries exist

## Slide 16: GPU Architecture
GPUs consist of Streaming Multiprocessors (SMs)
  NVIDIA calls these streaming multiprocessors and AMD calls them compute
units
SMs contain Streaming Processors (SPs) or Processing Elements (PEs)
  Each core contains one or more ALUs and FPUs
GPU can be thought of as a multi-multicore system
Adapted from NVIDIA Global Memory
Shared Memory |  |  | Shared Memory | 
Shared Memory |  |  | Shared Memory | 
Shared
Memory
Shared
Memory
Shared
Memory
Shared
Memory

## Slide 17: A Generic Modern GPU Architecture

## Slide 25: Fermi Architecture

## Slide 26: Fermi Architecture

## Slide 27: CUDA Programming

## Slide 28: What is CUDA?
It is general purpose parallel computing platform and programming model that leverages the parallel compute engine in NVIDIA GPUs
  Introduced in 2007 with NVIDIA Tesla architecture
  CUDA C, C++, Fortran, PyCUDA are language systems built on top of CUDA
Three key abstractions in CUDA
  Hierarchy of thread groups
  Shared memories
  Barrier synchronization

## Slide 32: Thread Hierarchy
A kernel executes in parallel across a set of parallel threads
All threads that are generated by a kernel launch are collectively called a grid
Threads are organized in thread blocks, and blocks are organized in to grids

## Slide 33: Thread Hierarchy
A thread block is a set of concurrently executing threads that can cooperate among themselves through barrier synchronization and shared memory
A grid is an array of thread blocks that execute the same kernel
  Read inputs to and write results to
global memory
  Synchronize between dependent kernel calls

## Slide 34: Dimension and Index Variables
Dimension
gridDim specifies the number of blocks in the grid
blockDim specifies the number of threads in each block
Index
blockIdx gives the index of the block in the grid
threadIdx gives the index of the thread within the block
Type is dim3

## Slide 35: Thread Hierarchy
threadIdx is a 3-component vector
  Thread index can be 1D, 2D, or 3D
  Thread blocks as a result can be 1D, 2D, or 3D
How to find out the relation between thread ids and threadIdx?
  1D: tid = threadIdx.x
  2D block of size (Dx, Dy): thread ID of a thread of index (x, y) is (x + yDx)
  3D block of size (Dx, Dy, Dz): thread ID of a thread of index (x, y, z) is
(x + yDx + zDxDy)

## Slide 36: Thread Hierarchy
Threads in a block reside on the same core, max 1024 threads in a block
Thread blocks are organized into 1D, 2D, or 3D grids
  Also called cooperative thread array
  Grid dimension is given by gridDim
variable
Identify block within a grid with the
blockIdx variable
  Block dimension is given by
blockDim variable

## Slide 37
Finding Thread IDs
i is local to
each thread

## Slide 38: CUDA Philosophy
SIMT philosophy
Single Instruction Multiple Thread
Computationally intensive
The time spent on computation significantly exceeds the time spent on transferring data to and from GPU memory
Massively parallel
The computations can be broken down into hundreds or thousands of
independent units of work

## Slide 39: CUDA Programming Model
Partition the problem into coarse sub-problems that can be solved independently
Assign each sub-problem to a “block” of threads to be solved in
parallel
Each sub-problem is also decomposed into finer work items that are
solved in parallel by all threads within the “block”

## Slide 40: Heterogeneous Computing
Host
CPU and its memory (host memory)
Device
GPU and its memory (device memory)

## Slide 41: Heterogeneous Computing
#include <iostream> #include <algorithm>
using namespace std;
#define N 1024
#define RADIUS 3
#define BLOCK_SIZE 16
global void stencil_1d(int *in, int *out) {
shared int temp[BLOCK_SIZE + 2 * RADIUS]; int gindex = threadIdx.x + blockIdx.x * blockDim.x; int lindex = threadIdx.x + RADIUS;
// Read input elements into shared memory
temp[lindex] = in[gindex];
if (threadIdx.x < RADIUS) {
temp[lindex - RADIUS] = in[gindex - RADIUS]; temp[lindex + BLOCK_SIZE] = in[gindex + BLOCK_SIZE];
}
// Synchronize (ensure all the data is available)
syncthreads();
// Apply the stencil int result = 0;
for (int offset = -RADIUS ; offset <= RADIUS ; offset++) result += temp[lindex + offset];
// Store the result out[gindex] = result;
}
void fill_ints(int *x, int n) { fill_n(x, n, 1);
}
int main(void) {
int *in, *out; // host copies of a, b, c
int *d_in, *d_out; // device copies of a, b, c int size = (N + 2*RADIUS) * sizeof(int);
// Alloc space for host copies and setup values
in = (int *)malloc(size); fill_ints(in, N + 2*RADIUS); out = (int *)malloc(size); fill_ints(out, N + 2*RADIUS);
// Alloc space for device copies cudaMalloc((void **)&d_in, size); cudaMalloc((void **)&d_out, size);
// Copy to device
cudaMemcpy(d_in, in, size, cudaMemcpyHostToDevice); cudaMemcpy(d_out, out, size, cudaMemcpyHostToDevice);
// Launch stencil_1d() kernel on GPU stencil_1d<<<N/BLOCK_SIZE,BLOCK_SIZE>>>(d_in + RADIUS,
d_out + RADIUS);
// Copy result back to host
cudaMemcpy(out, d_out, size, cudaMemcpyDeviceToHost);
// Cleanup free(in); free(out);
cudaFree(d_in); cudaFree(d_out); return 0;
}
serial code
parallel code serial code
parallel fn

## Slide 45: Kernels
GPU spawns m blocks with n threads (i.e., m*n threads total) that run a copy of the same function
CPU can continue processing while GPU runs kernel
Kernel call returns when all threads have terminated
kernel1<<<X,Y>>>(...); // kernel starts execution, CPU continues to next statement kernel2<<<X,Y>>>(...); // kernel2 placed in queue, will start after kernel1 finishes, CPU continues
cudaMemcpy(...); // CPU blocks until memory is copied, memory copy starts after all preceding CUDA calls finish
KernelName<<<m, n>>>(arg1, arg2, ...)

## Slide 46: Execution Model
Host (serial execution)
Device (Parallel execution)
Parallel kernel on device
Serial code on host Parallel kernel on device
Serial code on host

## Slide 47: Simple Processing Flow
PCI Bus

## Slide 48: Simple Processing Flow
1. Copy input data from CPU memory to GPU memory
PCI Bus

## Slide 49: Simple Processing Flow
Copy input data from CPU memory to GPU memory
Load GPU program and execute, caching data on chip for performance
PCI Bus

## Slide 50: Simple Processing Flow
Copy input data from CPU memory to GPU memory
Load GPU program and execute, caching data on chip for performance
Copy results from GPU memory to CPU memory
PCI Bus

## Slide 51: Hello World with CUDA
#include <stdio.h>
#include <cuda.h>
__global__ void hwkernel() { printf(“Hello world!\n”);
}
int main() {
hwkernel<<<1, 1>>>();
}
$ nvcc hello-world.cu
$./a.out
$

## Slide 52: Hello World with CUDA
#include <stdio.h>
#include <cuda.h>
global void hwkernel() { printf(“Hello world!\n”);
}
int main() {
hwkernel<<<1, 1>>>();
cudaDeviceSynchronize();
}
$ nvcc hello-world.cu
$./a.out Hello world!
$
Program returns immediately after launching the kernel. To prevent program to finish before kernel is completed, we call cudaDeviceSynchronize().

## Slide 53: Hello World with CUDA
#include <stdio.h>
#include <cuda.h>
global void hwkernel() { printf(“Hello world!\n”);
}
int main() { hwkernel<<<1, 32>>>();
cudaThreadSynchronize();
}
$ nvcc hello-world.cu
$./a.out Hello world! Hello world! Hello world! Hello world! Hello world!
…
…
$

## Slide 54: Function Declarations in CUDA
 | Executed on | Callable from
device float deviceFunc() | Device | Device
global void kernelFunc() | Device | Host
host float hostFunc() | Host | Host
global define a kernel function, must return void
device functions can have return values
host is default, and can be omitted
Prepending host device causes the system to compile separate host and device versions of the function

## Slide 55: How NVCC works?
Nvcc is a driver program based on LLVM
  Compiles and links all input files
  Requires a general-purpose C/C++ host compiler
    Uses gcc and g++ by default on Linux platforms
  nvcc --version
https://docs.nvidia.com/cuda/cuda-compiler-driver-nvcc/index.html

## Slide 56: NVCC Details
Important Options | Description
-std {c++03¦c++11¦c++14} | Select a particular C++ dialect
-m {32¦64} | Specify the architecture
-arch ARCH | Specify the class of the virtual GPU architecture
-code CODE | Specify the name of the GPU to assemble and optimize for
Input File Type | Description
.cu | CUDA source file
.c, .cpp, .cxx, .cc | C/C++ source files
.ptx | PTX intermediate assembly
.cubin | CUDA device binary code for a single GPU architecture
.fatbin | CUDA fat binary file that may contain multiple PTX and CUBIN files
.a, .so, .lib | …
NVIDIA. CUDA Compiler Driver NVCC. v11.1.

## Slide 57: Dynamic Parallelism
It is possible to launch kernels from other kernels
Calling global functions from the device is referred to as dynamic parallelism
  Requires CUDA devices of compute capability 3.5 and CUDA 5.0 or higher

## Slide 58: Vector Addition Example
global void VecAdd(float* A, float* B, float* C, int N) {
int i = blockDim.x * blockIdx.x + threadI dx.x;
if (i < N)
C[i] = A[i] + B[i];
}
int main() {
…
float* h_A = (float*)malloc(size); float* h_B = (float*)malloc(size); float* h_C = (float*)malloc(size);
float* d_A; cudaMalloc(&d_A, size); float* d_B; cudaMalloc(&d_B, size); float* d_C; cudaMalloc(&d_C, size);
// Copy vectors from host memory to
// device memory cudaMemcpy(d_A, h_A, size,
cudaMemcpyHostToDevice);
cudaMemcpy(d_B, h_B, size,
cudaMemcpyHostToDevice);

## Slide 59: Vector Addition Example
// Invoke kernel
int threadsPerBlock = 256;
int blocksPerGrid = N/threadsPerBlock;
VecAdd<<<blocksPerGrid, threadsPerBloc k>>>(d_A, d_B, d_C, N);
// Copy result from device memory to
// host memory cudaMemcpy(h_C, d_C, size,
cudaMemcpyDeviceToHost);
…
cudaFree(d_A); cudaFree(d_B); cudaFree(d_C);
…
}

## Slide 60: Typical CUDA Program Flow
Load data into CPU memory
  fread/rand
Copy data from CPU to GPU memory
  cudaMemcpy(..., cudaMemcpyHostToDevice)
Call GPU kernel
  yourkernel<<<x, y>>>(...)
Copy results from GPU to CPU memory.
  cudaMemcpy(..., cudaMemcpyDeviceToHost)
Use results on CPU

## Slide 61: CUDA Extensions for C/C++
Kernel launch
  Calling functions on GPU
Memory management
  GPU memory allocation, copying data to/from GPU
Declaration qualifiers
  device , shared, local, global , host
Special instructions
  Barriers, fences, etc.
Keywords
  threadIdx, blockIdx, blockDim

## Slide 62: C++11 Support from CUDA 7.5+
Supported Features
auto
lambdas
constexpr
rvalue references
range-based for loops
Unsupported Features
Standard library
  You cannot use std::cout in device code

## Slide 63: Kernels
Special functions that a CPU can call to execute on the GPU
  Executed N times in parallel by N
different CUDA threads
  Cannot return a value
Each thread will execute
VecAdd()
Each thread has a unique thread ID that is accessible within the kernel through the built-in threadIdx variable
// Kernel definition
__global__ void VecAdd(float* A, float* B, float* C) {
int i = threadIdx.x;
…
}
int main() {
…
// Kernel invocation with N threads VecAdd<<<1, N>>>(A, B, C);
}

## Slide 64: Find Device Information
int count; cudaError_t err =
cudaGetDeviceCount(&count);
if (err != cudaSuccess) {
cerr << cudaGetErrorString(err) << endl;
}
cudaDeviceProp Props;
for (int i = 0; i < count; i++) {
err = cudaGetDeviceProperties(&Props, i)
;
}
Device number: 3
Device name: GeForce GTX 1080 Ti Integrated or discrete GPU? discrete Clock rate: 1544 MHz
Compute capability: 6.1
Number of SMs: 28
Total number of CUDA cores: 3584 Max threads per SM: 2048
Max threads per block: 1024 Warp size: 32
Max grid size (i.e., max number of blocks): [2147483647,65535,65535]
Max block dimension: [1024,1024,64]
Total global memory: 11172 MB Shared memory per SM: 96 KB 32-bit registers per SM: 65536 Shared mem per block: 48 KB Registers per block: 65536
Total const mem: 64 KB L2 cache size: 2816 KB

## Slide 65: Device Management
Application can query and select GPUs
  cudaGetDeviceCount(int *count)
  cudaSetDevice(int device)
  cudaGetDevice(int *device)
  cudaGetDeviceProperties(cudaDeviceProp *prop, int device)
Multiple host threads can share a device
A single host thread can manage multiple devices
  cudaSetDevice(i) to select current device
  cudaMemcpy(…) for peer-to-peer copies

## Slide 66: Launching Kernels
// Kernel definition
global void MatAdd(float A[N][N], float B[N][N], float C[N][N]) {
int i = threadIdx.y;
int j = threadIdx.x; C[i][j] = A[i][j] + B[i][j];
}
int main() {
...
// Kernel invocation with one block of N * N * 1 threads int numBlocks = 1;
dim3 threadsPerBlock(N, N);
MatAdd<<<numBlocks, threadsPerBlock>>>(A, B, C);
...
}

## Slide 67: Execution Configuration
Assume data is of length N, and say the kernel execution configuration is <<<N/TPB, TPB>>>
  Each block has TPB threads
  There are N/TPB blocks
Suppose N = 64 and TPB = 32
  Implies there are 2 blocks of 32 threads
Dimension variables are vectors of integral type

## Slide 68: Launching Kernels
// Kernel definition
global void MatAdd(float A[N][N], float B[N][N], float C[N][N]) {
int j = int i = | blockIdx.x * blockDim.x blockIdx.y * blockDim.y | + + | threadIdx.x; threadIdx.y;
C[i][j] | = A[i][j] + B[i][j]; |  | 
}
int main() {
...
// Kernel invocation
dim3 threadsPerBlock(16, 16);
dim3 numBlocks(N / threadsPerBlock.x, N / threadsPerBlock.y); MatAdd<<<numBlocks, threadsPerBlock>>>(A, B, C);
...
}

## Slide 69: Execution Configuration Uses Integer Arithmetic
Assume data is of length N, and say the kernel execution configuration is <<<N/TPB, TPB>>>
  Each block has TPB threads
  There are N/TPB blocks
Suppose N = 64 and TPB = 32
  Implies there are 2 blocks of 32 threads
Dimension variables are vectors of integral type
Now assume N = 65
So now what?

## Slide 70: Execution Configuration Uses Integer Arithmetic
Ensure that the grid covers the array length
One strategy is to change the number of blocks from N/TPB to (N+TPB-1)/TPB to ensure rounding up

## Slide 71: Execution Configuration Uses Integer Arithmetic
Ensure that the grid covers the array length
One strategy is to change the number of blocks from N/TPB to (N+TPB-1)/TPB to ensure rounding up
This means that a thread index can exceed the maximum array index
Many examples use a control statement in the kernel to check for such corner cases

## Slide 72: What should be numBlocks?
const int Nx = 11; // not a multiple of threadsPerBlock.x
const int Ny = 5; // not a multiple of threadsPerBlock.y
////////////////////////////////////////////// dim3 threadsPerBlock(4, 3, 1);
dim3 numBlocks(x, y, z);
// assume A, B, C are allocated Nx x Ny float arrays matrixAdd<<<numBlocks, threadsPerBlock>>>(A, B, C);

## Slide 73: What should be numBlocks?
const int Nx = 11; // not a multiple of threadsPerBlock.x
const int Ny = 5; // not a multiple of threadsPerBlock.y
////////////////////////////////////////////// dim3 threadsPerBlock(4, 3, 1);
dim3 numBlocks((Nx+threadsPerBlock.x‐1)/threadsPerBlock.x,
(Ny+threadsPerBlock.y‐1)/threadsPerBlock.y, 1);
// | assume A, B, C | are allocated Nx x Ny float arrays
// | this call will | cause execution of 72 threads
// | 6 blocks of 12 | threads each
matrixAdd<<<numBlocks, threadsPerBlock>>>(A, B, C);

## Slide 74: Example
global void matrixAdd(float* A,
float* B, float* C) {
int i = blockIdx.x * blockDim.x + threadIdx.x; int j = blockIdx.y * blockDim.y + threadIdx.y;
// Guard against out of bounds array access
if (i < N && j < N)
C[i+N*j] = A[i+N*j] + B[i+N*j];
}

## Slide 75: Matrix Multiplication Example
int main() {
int SIZE = N * N;
cudaError_t status;
float *hostA, *hostB, *hostC;
hostA = (float*)malloc(SIZE * sizeof(f
loat));
hostB = (float*)malloc(SIZE * sizeof(f loat));
hostC = (float*)malloc(SIZE * sizeof(f loat));
float *deviceA, *deviceB, *deviceC;
status = cudaMalloc((void**)&deviceA,
SIZE * sizeof(float));
if (status != cudaSuccess) {
cerr << cudaGetErrorString(status) <
< endl;
}
status = cudaMalloc((void**)&deviceB, SIZE * sizeof(float));
status = cudaMalloc((void**)&deviceC,
SIZE * sizeof(float));

## Slide 76: Matrix Multiplication Example
status = cudaMemcpy(deviceA, hostA, SI ZE * sizeof(float), cudaMemcpyHostToDevi ce);
status = cudaMemcpy(deviceB, hostB, SI ZE * sizeof(float), cudaMemcpyHostToDevi ce);
dim3 blocksPerGrid(1, 1);
dim3 threadsPerBlock(N, N); matmulKernel<<<blocksPerGrid, threadsP
erBlock>>>(deviceA, deviceB, deviceC);
cudaMemcpy(hostC, deviceC, SIZE * size of(float), cudaMemcpyDeviceToHost);
…
cudaFree(deviceA); cudaFree(deviceB); cudaFree(deviceC);
free(hostA);
free(hostB);
…
}

## Slide 77: Matrix Multiplication Example
global void matmulKernel(float* A, float* B, float* C) {
int i = blockIdx.y * blockDim.y + threadIdx.y;
int j = blockIdx.x * blockDim.x + threadIdx.x;
float tmp = 0;
if (i < N && j < N) {
// Each thread computes one element of the matrix
for (int k = 0; k < N; k++) {
tmp += A[i * N + k] * B[k * N + j];
}
}
C[i * N + j] = tmp;
}

## Slide 78: Choosing Optimal Execution Configuration
The number of thread blocks in a grid is usually dictated by the size of the data being processed or the number of processors in the system
  It is okay to have a much greater number of threads
No fixed rule, needs exploration and experimentation
Choose number of threads in a block to be some multiple of 32

## Slide 79: Timing a CUDA Kernel
float memsettime; cudaEvent_t start, stop;
// initialize CUDA timer
cudaEventCreate(&start); cudaEventCreate(&stop); cudaEventRecord(start,0);
// CUDA Kernel
…
cudaEventRecord(stop,0); // stop CUDA timer cudaEventSynchronize(stop); cudaEventElapsedTime(&memsettime,start,stop); // in milliseconds std::cout << “Kernel execution time: “ << memsettime << “\n”; cudaEventDestroy(start);
cudaEventDestroy(stop);

## Slide 80: Reporting Errors
All CUDA API calls return an error code (cudaError_t)
  Error in the API call itself or error in an earlier asynchronous operation (e.g. kernel)
Get the error code for the last error
cudaError_t cudaGetLastError(void)
Get a string to describe the error:
char *cudaGetErrorString(cudaError_t)

## Slide 81: Mapping Blocks and Threads
A GPU executes one or more kernel grids
When a CUDA kernel is launched, the thread blocks are enumerated and distributed to SMs
  Potentially >1 block per SM
An SM executes one or more thread blocks
  Each GPU has a limit on the number of blocks that can be assigned to each SM
  For example, a CUDA device may allow up to eight blocks to be assigned to
each SM
  Multiple thread blocks can execute concurrently on one SM

## Slide 82: Mapping Blocks and Threads
The threads of a block execute concurrently on one SM
  CUDA cores in the SM execute threads
A block begins execution only when it has secured all execution resources necessary for all the threads
As thread blocks terminate, new blocks are launched on the vacated multiprocessors
Blocks are mostly not supposed to synchronize with each other
  Allows for simple hardware support for data parallelism

## Slide 83: Memory Access Efficiency
Compute to global memory access ratio
  Number of floating-point operations performed for each access to global memory
for (int i = 0; i < N; i++) tmp += A[i*N+K]*B[k*N+j];
Assume a GPU device with 1 TB/s global memory bandwidth and peak single-precision performance of 12 TFLOPS
  What is the performance we expect with a ratio of 1?

## Slide 84: Memory Hierarchy in CUDA

## Slide 85: Variable Type Qualifiers in CUDA
 |  | Memory | Scope | Lifetime
int localVar |  | Register | Thread | Kernel
device | local int localVar | Local | Thread | Kernel
device | shared int sharedVar | Shared | Block | Kernel
device | int globalVar | Global | Grid | Application
device | constant int constVar | Constant | Grid | Application
device is optional when used with local , shared , or constant
Automatic variables without any qualifier reside in a register
  Except arrays that reside in local memory
Pointers can only point to memory allocated or declared in global memory

## Slide 86: Memory Organization
Host and device maintain their own separate memory spaces
  A variable in CPU memory may not be accessed directly in a GPU kernel
It is programmer's responsibility to keep them in sync
  A programmer needs to maintain copies of variables

## Slide 93: Registers
64K 32-bit registers per SM
  So 256KB register file per SM, a CPU in contrast has a few (1-2 KB) per core
Up to 255 registers per thread (compute capability 3.5+)
If a code uses the maximum number of registers per thread (255) and an SM has 64K of registers then the SM can support a maximum of 256 threads
If we use the maximum allowable number of threads per SM (2048), then each thread can use at most 32 registers per thread

## Slide 94: Shared Memory
Shared memory aims to bridge the gap in memory speed and access
  Also called scratchpad memory
  Usually 16-64KB of storage that can be accessed efficiently by all threads in a block
Primary mechanism in CUDA for efficiently supporting thread cooperation
Each SM contains a single shared memory
  Resides adjacent to an SM, on-chip
  The space is shared among all blocks running on that SM

## Slide 95: Shared Memory
Variable in shared memory is allocated using the shared specifier
  Faster than global memory
  Can be accessed only by threads
within a block
Amount of shared memory per block limits occupancy
Say an SM with 4 thread blocks has 16 KB of shared memory
shared float min[256]; shared float max[256]; shared float avg[256]; shared float stdev[256];

## Slide 96: Registers vs Shared Memory
Registers
Faster than shared memory
Private to a thread
Shared Memory
On-chip memory space, requires load/store operations
Visible to all threads in a block

## Slide 97: Global Variables
Variable lock can be accessed by both kernels
  Resides in global memory space
  Can be both read and modified by all threads
device int lock=0;
global void kernel1(...) {
// Kernel code
}
global void kernel2(...) {
// Kernel code
}

## Slide 98: Global Memory
On-device memory accessed via 32, 64, or 128 B transactions
An warp executes an instruction that accesses global memory
  The addresses are coalesced into transactions
  Number of transactions depend on the access size and distribution of memory addresses
  More transactions mean less throughput
    For example, if 32 B transaction is needed for a thread’s 4 B access, throughput is
essentially 1/8th

## Slide 99: Constant Memory
Used for data that will not change during kernel execution
  Constant memory is 64KB
Constant memory is cached
  Each SM has a read-only constant cache that is shared by all cores in the SM
  Used to speed up reads from the constant memory space which resides in
device memory
  Read from constant memory incurs a memory latency on a miss
    Otherwise, it is a read from constant cache, which is almost as fast as registers

## Slide 100: Constant Variables
Constant variables cannot be modified by kernels
  Reside in constant memory
  Accessible from all threads within a grid
They are defined with global scope within the kernel using the prefix
constant
Host code can access via cudaMemcpyToSymbol() and
cudaMemcpyFromSymbol()

## Slide 101: Local Memory
Local memory is off-chip memory
  More like thread-local global memory, so it requires memory transactions and consumes bandwidth
Automatic variables are placed in local memory
  Arrays for which it is not known whether indices are constant quantities
  Large structures or arrays that consume too much register space
  In case of register spilling
Inspect PTX assembly code (compile with –ptx)
  Check for ld.local and st.local mnemonic

## Slide 102: Device Memory Management
Global device memory can be allocated with cudaMalloc()
Freed by cudaFree()
Data transfer between host and device is with cudaMemcpy()
Initialize memory with cudaMemset()
There are asynchronous versions

## Slide 103: GPU Caches
GPUs have L1 and L2 data caches on devices with CC 2.x and higher
  Texture and constant cache are available on all devices
L1 cache is per SM
  Shared memory is partitioned out of unified data cache and its size can be configured, remaining portion is the L1 cache
  Can be configured as 48 KB of shared memory and 16 KB of L1 cache, or 16 KB of shared memory and 48 KB of L1 cache, or 32 KB each
  L1 caches are 16-48 KB
L2 cache is shared by all SMs
L1 cache lines are 128 B wide in Fermi onward, while L2 lines are 32 B

## Slide 104: CPU Caches vs GPU caches
CPU
Data is automatically moved by hardware between caches
  Association between threads and cache does not have to be exposed to programming model
Caches are generally coherent
GPU
Data movement must be orchestrated by programmer
  Association between threads and storage is exposed to programming model
L1 cache is not coherent, L2 cache is coherent